## Slide 1
©CRIEPI
The national framework for the management of foodstuff in Japan following the Fukushima accident
Radiation Safety Research Center, Nuclear Technology Research Laboratory,
Central Research Institute of Electric Power Industry (CRIEPI), Tokyo, Japan
22 May 2013
CIEMAT, Madrid, Spain
The 2nd Meeting of
the NERIS Working Group on Contaminated goods (ConGoo)
Nobuyuki Hamada,
Haruyuki Ogino, and Yuki Fujimichi
<number>
Notes: <number>

## Slide 2
©CRIEPI
Radiation Safety Research Center, Nuclear Technology Research Laboratory,
Central Research Institute of Electric Power Industry (CRIEPI), Tokyo, Japan
Nobuyuki Hamada,
Haruyuki Ogino, and Yuki Fujimichi
<number>
Notes: <number>

## Slide 3
The Great East Japan Earthquake
<number>
Occurred off the northeastern coast of Japan at 14:46 (Japan Standard Time) on 11 March 2011.
Registered a moment magnitude of 9.0 (fourth largest in the world).
Unleashed a substantial tsunami as high as 40.5 m reportedly that traveled to as far as 10 km inland.
Caused a massive destruction across a wide area: there have been 15,883 confirmed fatalities with 2,676 people missing as of 10 May 2013.
And led to the first-ever declaration of nuclear emergency situation at the Fukushima nuclear power plant 1 at 19:03 on 11 March 2011, and Nuclear Emergency Response Headquarters (NERHQ) was established on the same day.
Notes: <number>

## Slide 4
Fukushima nuclear accident
<number>
Upon the quake, all operating plants underwent automatic shutdown.
The emergency diesel generators successfully started to supply power for nuclear fuel cooling system.
At about 1 h after the quake, the 14 m high tsunami overwhelmed the site’s sea defenses designed to withstand 5.7 m high tsunamis, and generators become inoperable.
Elevation of temperature and pressure inside the reactors resulted in a partial meltdown and hydrogen explosions, followed by the radionuclide discharges.
The first discharge was recorded on the early morning of 12 March 2011.
Discharge into the atmosphere
160 PBq of 131I, 18 PBq of 134Cs, 15 PBq of 137Cs (11-16 March 2011)
Discharge into sea (a total of 131I, 134Cs and 137Cs )
4.7 PBq (1-6 April 2011), 150 GBq (4-10 April 2011), 20 TBq (11 May 2011)
Notes: <number>

## Slide 5
Fukushima vs Chernobyl
<number>
Commonality
The Fukushima and Chernobyl were both rated at the top level 7 on the International Nuclear and Radiological Event Scale (INES).
Difference
In the Fukushima accident (compared with the Chernobyl accident),
the amount of discharged radionuclides was about one-seventh,
radionuclide releases continued over a longer period of time
(e.g., until cold shutdown in December 2012 or even later, albeit major
releases in the first one month),
and the dose posed by internal exposure was much lower (details will be provided later).
Notes: <number>

## Slide 6
Stable iodine
<number>
On 16 March 2011, NERHQ gave the Governor of the Fukushima Prefecture instruction that evacuees aged <40 years leaving the stay-away evacuation zone to take stable iodine.
However, the Fukushima Prefecture did not pass this instruction to its municipalities to distribute stable iodine, so that evacuees failed to receive and take stable iodine.
(Nb., there is an exception for several municipalities (Futaba, Tomioka, Okuma, Miharu towns) where local governments distributed stable iodines without awaiting NERHQ’s instruction and some of those pills were taken).
Notes: <number>

## Slide 7
Initial responses for food and water
<number>
15 March 2011
Preliminary surveys revealed that high levels of radioiodines and radiocesiums were detected, so that the Nuclear Safety Commission (NSC) advised that monitoring surveys of food and water should begin immediately.
17 March 2011
Ministry of Health Labour and Welfare (MHLW) set regulatory limits stipulated as “provisional regulation values”.
21 March 2011
The first restrictions on distribution and consumption were imposed.
Notes: <number>

## Slide 8
Provisional regulation value (PRV)
<number>
20 March 2011
MHLW asked Food Safety Commission (FSC) to assess the validity of PRV.
29 March 2011
FSC guaranteed that PRV set by MHLW is effective enough to ensure safety.
4 April 2011
MHLW decided to use for the meantime
PRV was set for radioiodines, radiocesiums, uranium, plutonium and other transuranic alpha emitters.
Of these, my talk focuses on radioiodines and radiocesiums, because other radionuclides did not exceed PRV.
Notes: <number>

## Slide 9
PRV for radioiodines
<number>
PRV in water and milk ingested by infants was adopted from the guideline level indicated by the Codex Alimentalius Commission in 1995.
RPV in aquatic products was newly set on 5 April 2011 by adapting the value for vegetables, because radioiodines at levels of concern were detected in fish sampled on 1 April 2011.
Other values were derived from the “index values” that NSC had provided as evaluation criteria to launch discussion on whether NERHQ needs to restrict the consumption of food and water.
Values were defined in water, and two categories of food (milk and vegetables), but not for other food.
Intervention level/category considered was a committed equivalent dose to the thyroid of 11.1 mSv/year.
Index values were calculated as radioactive concentrations of indicator radionuclides (131I) by postulating the relative radioactive concentration of coexisting radionuclides (132I, 133I, 134I, 135I and 132Te).
Notes: <number>

## Slide 10
PRV for radiocesiums
<number>
All values were derived from the index values.
Values were defined in water, and five categories of food (i.e., all food).
Intervention level/category considered was a committed effective dose of 1 mSv/year.
Index values were calculated as radioactive concentrations of indicator radionuclides (134Cs and 137Cs) by postulating the relative radioactive concentration of coexisting radionuclides (89Sr and 90Sr).
Notes: <number>

## Slide 11
PRV for radioiodines and radiocesiums
<number>
According to PRV, the levels of indicator radionuclides were only monitored.
RPV was used until 31 March 2012 albeit “provisional”.
So let’s see the food safety regulations implemented until 31 March 2012.
Notes: <number>

## Slide 12
Areas of concern
<number>
17 prefectures of which name is indicated in the map were assigned as target local governments for food monitoring surveys.
Gray-colored area emphasizes prefectures in which restrictions on distribution and/or consumption of food and/or water were implemented.
* denotes the Fukushima nuclear
power plant 1.
Notes: <number>

## Slide 13
Brief outline of regulations
<number>
Water
MHLW instructed and lifted restrictions on consumption (distribution restrictions were not instructed).
PRV was exceeded in 68 samples among 83,074 samples of which monitoring data was reported between 21 March 2011 and 31 March 2012.
Food
NERHQ imposed and removed restrictions on distribution and consumption, taking into account the advice from NSC as to the necessity of restrictions.
PRV was exceeded in 1,519 samples among 137,337 samples of which monitoring data was reported between 19 March 2011 and 31 March 2012.
Clear criteria were provided to remove restrictions, but not to order them.
Namely, concrete boundary values of radioactive concentrations for “highly contaminated food” and “very highly contaminated food” were not defined to restrict distribution and consumption, respectively.
Notes: <number>

## Slide 14
Brief outline of regulations
<number>
PRV for radioiodines was exceeded in tap water and food sampled from 16 March 2011 to 21 May 2011 (i.e., 67 days).
However, it remains unclear whether contamination at levels of concern had occurred on 12-15 March 2011.
Maximum concentration of 131I detected was 54,100 Bq/kg in spinach sampled in Ibaraki Prefecture on 18 March 2011 (max in Fukushima = 22,000 Bq/kg).
PRV for radiocesiums was exceeded in tap water and food sampled from 18 March 2011 to 31 March 2012.
Maximum total concentration of 134Cs and 137Cs detected was 82,000 Bq/kg in kukitachi-na sampled in Fukushima Prefecture on 21 March 2011.
PRV was initially exceeded in tap water, raw milk and leafy vegetables, and subsequently in other foodstuffs such as mushrooms, aquatic products, beef and tea leaves.
Coastal fish that inhabit the deeper sea tended to become contaminated at a later time.
Notes: <number>

## Slide 15
Brief outline of regulations
<number>
It took 6 and 7 days to start sampling food and water for monitoring surveys, and to set RPV, respectively, after the establishment of the NERHQ.
The first restrictions were instructed 11 days after the establishment of the NERHQ.
All restrictions were instructed within 318 days of PRV first being exceeded in each item.
A partial removal of restrictions (restrictions for each lot) was conducted for beef and wild boar meat.
Brown rice but not polished rice exceeded PRV for radiocesiums regardless of three-stage strategies (i.e., cultivation restrictions, pre-harvest survey and post-harvest survey).
Notes: <number>

## Slide 16
Restrictions implemented in Fukushima
<number>
Most foodstuffs contaminated above PRV were restricted except seafood.
Contaminated seafood items were not restricted except konago fish, but were not distributed because fishing was restricted.
Once enforced, many restrictions were not removed for a long period of time after PRV was last exceeded.
Such long-term restrictions may affect the sustainable development and rehabilitation of the affected areas.
Notes: <number>

## Slide 17
Experience for beef
<number>
On 19 March 2011, Ministry of Agriculture, Forestry and Fisheries (MAFF) provided directives to prevent or minimize exposure of farm animals to radioactive materials.
On 14 April 2011, MAFF set the provisional tolerance values (PTV) to minimize contamination of milk and beef by regulating contaminated livestock feed for daily cattle.
On 8 July 2011, the first beef sample that exceeded PRV was reported.
On 2 September 2011, it became known that the beef from cattle slaughtered as far back as 30 March 2011.
Distributed beef was recalled but most of them from the cattle slaughtered by July 2011 had already been consumed.
Such contamination of beef resulted from the highly contaminated rice straw (reportedly ~690,000 Bq/kg of radiocesiums) being fed to cattle. Though MAFF had provided directives and PTV, farmers had not been well notified regarding the rice straw.
Notes: <number>

## Slide 18
Social dislocations
<number>
The beginning of restrictions in March 2011 was concurrent with the massive social dislocations that were manifested as the selling out of bottled water, milk, instant noodles and various non-perishables.
Take, drinking water, for instance.
Due to buy-up, bottled drinking water disappeared from the grocery stores in many prefectures even where radionuclide concentrations in tap water were below detectable levels.
On 23 March 2011, the Tokyo Metropolitan government decided to mitigate the social dislocations by distributing 240,000 bottles of drinking water for free to ~80,000 infant residents of Tokyo Metropolis.
The maximum level detected in tap water sampled in Tokyo was 210 Bq/kg of 131I. This was above PRV (i.e., 100 Bq/kg, Codex’s guideline level) but still below the index value (300 Bq/kg).
Such experience for beef and social dislocations highlights the importance of strategies for effective communications between the risk management authorities and individuals concerned.
Notes: <number>

## Slide 19
Dose posed by internal exposure
<number>
Radioiodines
In late March 2011, surveys of 1,149 children living in Fukushima were conducted, and a maximum level detected was a committed equivalent dose to the thyroid of 43 mSv.
Radiocesiums
In June-October 2011, surveys of 6,608 people were conducted (measured by whole body counter)
1-3 mSv: 19 individuals (0.3%)
<1 mSv: 6,589 individuals (99.7%)
Dose posed by internal exposure is much lower than the Chernobyl accident.
All together, it can be concluded that food safety regulations were successfully implemented following the Fukushima accident.
Notes: <number>

## Slide 20
Change to new regulation values
<number>
New values were promulgated on 15 March 2012, and became effective on 1 April 2012.
Values were defined as a total radioactive concentration of 134Cs and 137Cs not to exceed a committed effective dose of 1 mSv/year (stems from lifetime effective dose of 100 mSv), considering the contributions of 90Sr, 238Pu, 239Pu, 240Pu and 106Ru where physical half-life is ≥1 year (radioiodines were not considered).
This is the intervention level, but not the reference level.
Notes: <number>

## Slide 21
Ongoing regulations and restrictions
<number>
1 April 2012 to 31 March 2013 (Fiscal Year 2012)
New regulation values were exceeded in 2,372 samples out of
278,275 samples.
Of these, 17 samples exceeded PRV for radiocesiums.
1 April 2013 to 21 May 2013 (Fiscal Year 2013)
New regulation values were exceeded in 170 samples out of
43,645 samples.
As of 21 May 2013
In Fukushima Prefecture, consumption of leafy vegetables, wild mushrooms, yamame fish, and wild boar meat, and distribution of various foodstuff items have been restricted.
In other 13 prefectures, distribution of vegetables, mushrooms, cereal,
fish, and meat have been imposed.
Notes: <number>

## Slide 22
Impact on European legislation
<number>
17 March 2011
MHLW set PRV.
25 March 2011
EC. Commission Implementing Regulation (EU) No. 297/2011.
11 April 2011
EC. Commission Implementing Regulation (EU) No. 351/2011.
Chernobyl regulatory limits (No. 3954/1987) were basically resurrected.
This led to a discrepancy, such that, whereas a limit for radiostrontiums was set for imports from Japan, Japan has not conducted monitoring surveys and has not set a limit for radiostrontiums.
17 June 2011
It was reported that at the Paris Charles de Gaulle Airport, 1,038 Bq/kg of radiocesiums exceeding the EU’s maximum permitted level of 500 Bq/kg (= PRV) were detected in dried tea leaves that were shipped as a lot of 162 kg from Shizuoka Prefecture. On 22 June 2011, Shizuoka Prefecture confirmed 981 Bq/kg of radiocesiums in the same lot, and so recalled the products.
Notes: <number>

## Slide 23
Impact on European legislation
<number>
15 March 2012
MHLW promulgated new regulation values.
29 March 2012
EC. Commission Implementing Regulation (EU) No. 284/2012.
On one hand, limits for radiostrontiums, plutonium and americium were now excluded.
On the other, there is a discrepancy again, such that, for radiocesiums in adult food, limits are 10-100 Bq/kg for imports from Japan, but 600 Bq/kg for agricultural products that become contaminated with fallout from the Chernobyl accident and originate within European countries (EC No. 733/2008).
Notes: <number>

## Slide 24
Published source of our thoughts
<number>
Hamada N, Ogino H. Food safety regulations: what we learned from
the Fukushima nuclear accident. J Environ Radioact 111 (2012) 83-99.
Hamada N, Ogino H, Fujimichi Y. Safety regulations of food and water
implemented in the first year following the Fukushima nuclear accident.
J Radiat Res 53 (2012) 641-671.
Merz S, Steinhauser G, Hamada N. Anthropogenic radionuclides in
Japanese food: environmental and legal implications.
Environ Sci Technol 47 (2013) 1248-1256.
Notes: <number>

## Slide 25
We hope that the lessons learned from the Fukushima accident should help improve the nuclear or emergency preparedness all over the world.
<number>
Notes: <number>

## Slide 26
Thank you for your attention
and
I am happy to answer your questions
<number>
Notes: <number>

## Slide 27
©CRIEPI
The national framework for the management of foodstuff in Japan following the Fukushima accident
Radiation Safety Research Center, Nuclear Technology Research Laboratory,
Central Research Institute of Electric Power Industry (CRIEPI), Tokyo, Japan
22 May 2013
CIEMAT, Madrid, Spain
The 2nd Meeting of
the NERIS Working Group on Contaminated goods (ConGoo)
Nobuyuki Hamada,
Haruyuki Ogino, and Yuki Fujimichi
<number>
Notes: <number>