## Slide 1
CONFIDENCE WP1
Achievements and perspectives
Irène Korsakissok, IRSN

## Slide 2: Initial goals
To determine and (if possible) quantify all sources of uncertainties that have an impact on atmospheric dispersion outputs
To propagate these uncertainties through Atmospheric Dispersion Models for several scenarios in order to
  Evaluate how input uncertainties influence the outputs (dose…)
  Compare the ensemble outputs
  Compare the outputs to radiological observations (Fukushima)
To propose ways of using this ensemble approach in an operational context for emergency response, including
  Making practical recommendation on which uncertainties to take into account and how to do it
  Reducing the computational time in an acceptable way
  Proposing indicators and maps to present these uncertainties

## Slide 3: Challenges
Huge amount of data
  Takes time to generate, upload/download, process…
  Challenge for operational use
Timing
  Time to work on input uncertainties (meteo / source term / models)
  Time to discuss and determine the (5) accident scenarios
  Time to generate the data…
  Time for all participants (up to 7 per case study) to run the simulations simultaneously…
  Time to process results from all participants (huge amount of data!)
  … while trying to provide some inputs to other WPs early enough in the project
This challenge was taken up and became a success thanks to the great involvement and enthusiasm of all participants!

## Slide 4: Achievements
Input uncertainties have been detailed and ranked in a comprehensive manner
Ensemble capabilities were implemented in all participating countries (at least on a demonstration level)
Ensemble inter-comparisons were carried out on the case studies and lead to several findings:
  Importance of taking into account source term uncertainties (especially release time), not only meteorological ones
  Inter-ensemble variability was not negligible, especially in cases where other uncertainties are low
  Indicators were proposed for ensemble evaluation by comparison to observations

## Slide 5: Recommendations for operational use
Use ensembles! Trying to define a “worst case” a priori is not a good idea.
Reduce computational time
  By simplifying model configurations (domain, number of puffs/particles, number of radionuclides…)
  By clustering ensemble members (i.e. grouping them in an intelligent manner) with respect to dispersion endpoints (and not based on a priori resemblance between source terms or meteorological fields)
A spread of uncertainty indicators and presentation methods is vital to fully understand model endpoint uncertainties which are spatially and temporally complex

## Slide 6: Pending questions (1)
Source term uncertainties have been demonstrated to be of prime importance, but we are far from having a proper quantification of these uncertainties in an emergency context
  Preliminary demonstration using ensemble of source terms from FASTNET
  Sometimes it might not be possible (”deep uncertainties”) but working on the subject is vital
  Necessity to set up a framework for discussion between “source term experts” and “dispersion experts”

## Slide 7: Pending questions (2)
Meteorological uncertainties can be taken into account using meteorological ensembles but… we still have questions
  Ensemble resolution: is it better to have a high-resolution ensemble or more members with a crude resolution?
  Temporal continuity: how to do ensure the temporal continuity of the members in case a long period of forecast is needed ?
  How to design ensembles better suited to our purpose (i.e. more representative of the uncertain variables that are used in dispersion)?
Operational use: still a lot of work to do to develop efficient ways of running computationally cheap ensemble simulations
  Determine a methodology for simplifying model runs, focused on the primary outputs required, including high-level tools such as emulators
  Develop automated clustering methods fit for our purpose

## Slide 8: Pending questions (3)
Using dispersion field studies for ensemble evaluation would allow us to
  Consider other spatial scales than Fukushima
  Evaluate ensembles for other geographical areas
  Use case studies without source term uncertainties
  To gain knowledge on the overall ensembles’ performance
  To use as a feedback (calibration, for instance using Bayesian methods) in order to improve our evaluation of input uncertainties
What about uncertainties at other scales? For instance, what about the use of CFD models at very local scale (10-100m) in urban areas?

## Slide 9: To conclude…
Real team work between the different participants from 8 countries
Bringing together meteorologists and dispersion modellers
Several (hundreds of?) TB of data processed
Lively discussions
Everyone learned from the others (I certainly did)
An experience to be (hopefully) continued in a next project!
Thank you!